## Slide 1
[YYYY/MM]
「Course」
[Course name]
1
[Author]
「 Lesson 5 」 Secure file transfer and results

## Slide 2
2
Today’s lesson purpose:
Use the key from the handshake: an encrypted channel that streams a file of any size from one board's SD card to the other's.
Make the radio link and the SD card reliable — and learn from the bugs we hit.
Measure where the time goes, make it faster, and see how each question behind the project was answered.
Code: fpga/sw/export/common (edhoc_app_data, edhoc_rf_link, sd_card, fat32, edhoc_file_xfer)

## Slide 3
Outline
3
Application Channel
Radio Link
SD Card & FAT32
End-to-End Transfer
Making It Faster
Questions Behind the Project
Practice

## Slide 4
Outline
4
Application Channel
Radio Link
SD Card & FAT32
End-to-End Transfer
Making It Faster
Questions Behind the Project
Practice

## Slide 5
1. Application Channel (1/4) Keys for the application
5
PRK_out
(EDHOC)
PRK_exporter
K_app = Exporter(32768)
IV_app = Exporter(32769)
Same suite, same keys on both boards — nothing secret is sent.
The AEAD is the suite's application AEAD: AES-CCM-16-64-128, AES-128/256-GCM or ChaCha20/Poly1305; key, IV and tag sizes are read at run time, so one code path serves every suite.
The file demo runs with AuthKEM TBD3: AES-256-GCM, 32-byte key.

## Slide 6
1. Application Channel (2/4) One record
6
Part | Content | Sent?
header (5 B) | direction (0 = A→B, 1 = B→A) ‖ 32-bit sequence number | no — both sides know it
nonce | IV_app XOR header (in the last 5 bytes) | no
ciphertext | AEAD(K_app, nonce, aad = header, plaintext ≤ 206 B) | yes
tag | 8 or 16 bytes | yes
common/src/edhoc_app_data.c
static void mk_nonce(const struct app_chan *ch, uint8_t *nonce, const uint8_t *hdr)
{
uint32_t off = ch->iv_len - APP_HDR_LEN;
memcpy(nonce, ch->base_iv, ch->iv_len);
for (uint32_t i = 0; i < APP_HDR_LEN; i++)
nonce[off + i] ^= hdr[i];
}
The two directions never share a nonce.
A lost, repeated or reordered record fails its tag.

## Slide 7
1. Application Channel (3/4) Using it from your code
7
common/include/edhoc_app_data.h
struct app_chan ch;
app_data_init(&ch, suite, &prk_out, is_initiator); // keys from PRK_out
app_data_send(&ch, buf, len, tx, sock); // len <= APP_PT_MAX (206)
app_data_recv(&ch, buf, sizeof(buf), &got, rx, sock); // decrypt + verify
tx / rx are the same transport functions as the handshake (radio or UART).
Records are at most 206 bytes: 206 + 16-byte tag fills exactly two radio fragments (section 2).
Every send and receive also adds to an encrypt / decrypt cycle counter — the PERF encrypt / PERF decrypt lines.

## Slide 8
1. Application Channel (4/4) Demo traffic
8
initiator, TBD3
APP: channel up (aead=3 key=32 iv=12 tag=16)
APP: sent 'REQ 0 FROM INITIATOR'
APP: got 'ECHO[REQ 0 FROM INITIATOR]'
APP: sent 'REQ 1 FROM INITIATOR'
APP: got 'ECHO[REQ 1 FROM INITIATOR]'
...
PERF encrypt 89688 cyc 0.001195 s 60 bytes 50209 B/s
APP DATA OK
After every handshake: three requests and echoes both ways prove both keys and both directions.
Then, depending on the build:
APP_FILE_BYTES=n — stream n generated bytes (checked by regenerating them)
-DAPP_SD_XFER — send SEND.BIN card to card (section 4)

## Slide 9
Outline
9
Application Channel
Radio Link
SD Card & FAT32
End-to-End Transfer
Making It Faster
Questions Behind the Project
Practice

## Slide 10
2. Radio Link (1/8) The MRF24J40 and its limits
10
Property | Value | Consequence
Standard | IEEE 802.15.4, 2.4 GHz, channel 11 | shared band with Wi-Fi
Bit rate | 250 kbit/s (32 µs per byte) | ≈ 4 ms on air for a full frame
Frame | 127 B → 116 B payload after the 802.15.4 header | a record needs 2 frames
Receive buffer | one frame | the sender must wait until the receiver read it
Host interface | SPI at 4.7 MHz over PMOD wires | bit errors happen (next slides)
Hardware ACK: the radio confirms the frame reached the peer's receive buffer.
It does not confirm the peer's software read it — that needs our own ACK.

## Slide 11
2. Radio Link (2/8) Fragments and stop-and-wait
11
common/include/edhoc_rf_link.h
frame payload = [type][seq][flags][data ... up to 111 B][crc16]
type 'D' data fragment flags bit0 = first, bit1 = last of the message
'A' acknowledgement of fragment seq
A → B
'D' seq k
B
read, CRC ok
B → A
'A' seq k
A → B
'D' seq k+1
The next fragment goes out only after the 'A' for the previous one.
No 'A' within 30 ms → send the same fragment again; the receiver re-acks a repeat and drops it.
Simple and safe with a one-frame receive buffer; the price is one round trip per fragment.

## Slide 12
2. Radio Link (3/8) One radio frame, byte by byte
12
Bytes | Field | Written by
2 | frame control: data frame, ACK request, PAN ID compression, short addresses | mrf24j40.c
1 | 802.15.4 sequence number | mrf24j40.c
2 | PAN ID 0xABCD | mrf24j40.c
2 + 2 | destination / source short address | mrf24j40.c
3 | link header: type 'D' or 'A', seq, flags (bit 0 FIRST, bit 1 LAST) | edhoc_rf_link.c
≤ 111 | data | edhoc_rf_link.c
2 | CRC-16/CCITT over link header + data | edhoc_rf_link.c
2 | FCS (802.15.4 CRC) | radio chip
9 + 3 + 111 + 2 + 2 = 127 bytes, the largest 802.15.4 frame.
Two checksums: the FCS covers the air, our CRC-16 also covers the SPI wires on both sides (Problem 1). Our 'A' frame is 16 bytes: header, link header, CRC, FCS.

## Slide 13
2. Radio Link (4/8) Splitting and rebuilding a message
13
common/src/edhoc_rf_link.c (shortened)
int32_t rf_link_recv(uint8_t *data, uint32_t cap)
{
len = recv_frag(f); // next 'D' in order, already ACKed
if (!(f[2] & F_FIRST)) return -2; // must start a message
for (;;) {
copy f[3 .. len) to data + got; // -2 if it would pass cap
if (f[2] & F_LAST) return got; // message complete
len = recv_frag(f);
if (f[2] & F_FIRST) return -2; // a new message inside this one
}
}
Message | Bytes | Fragments
app record: 206 B + 16-B tag | 222 | 111 FIRST, 111 LAST
length / CRC record: 4 B + tag | 20 | 1 (FIRST + LAST)
RFC 9529 message_2 | 45 | 1
TBD3 message_4 | 1,604 | 14 × 111 + 50 = 15
seq is 8 bits and wraps at 256: safe, because only one fragment is ever unconfirmed.
A repeat of the fragment accepted last (its 'A' was lost) is acknowledged again and dropped, so data is never delivered twice.
The first fragment of the peer's next message also confirms our last one (implicit ACK, take_reply()).

## Slide 14
2. Radio Link (5/8) Problem 1: corrupted bytes
14
Symptom | the first 1 MiB stream failed after ~80 s with an AEAD tag error (113) — no SD card involved
Observation | the radio had acknowledged the frame, so its FCS was valid; the bytes the receiver decrypted were not the bytes sent
Cause | a bit flips now and then on the SPI wires between CPU and radio. The radio computes its FCS after the flip, so it cannot see it
Fix | our own CRC-16 per frame (seal() / poll_frame() in edhoc_rf_link.c), computed before SPI on the way out and checked after SPI on the way in; a bad frame gets no 'A' and is sent again
Check it | the RF: line at the end of every run counts crc_err. A long transfer with crc_err > 0 that still ends in XFER RECV … OK shows the CRC catching and recovering
Lesson | check data end to end yourself; a link layer's checksum covers only its own part of the path

## Slide 15
2. Radio Link (6/8) Problem 2: a radio goes deaf
15
Symptom | with the CRC in place, the stream then stopped for good after ~420 KB
Observation | the sender repeated one fragment 9,140 times; the receiver received nothing at all
Cause | inference, not observed directly: a flipped SPI write left a radio control register wrong (e.g. the channel). A data CRC cannot repair that
Fix | a watchdog (heal_if_stuck): no progress for 2 s → reset and re-program the radio, keeping all sequence numbers. It must run in every waiting loop — the first version missed the transmit retry loop
Check it | the RF: line counts reinits. The responder shows a few while it waits for the initiator to be loaded (2 s each) — harmless; in a long transfer, reinits > 0 with a completed transfer shows recovery
Lesson | recover from stuck hardware instead of trusting it: every wait needs a way out

## Slide 16
2. Radio Link (7/8) Problem 3: both sides repeating
16
Symptom | with DEBUG=1 builds the pair hung right after the handshake; also with a normal build when the initiator paused 0.5 s
Observation | read over JTAG: both boards in the transmit loop, each repeating one frame ~40 times a second, never acknowledged (TX status 0xC1); the watchdog did not help
Cause | a radio holding an unread frame in its one-frame FIFO was seen to acknowledge nothing — and neither side read its FIFO while repeating. Same root: a board that had finished left its peer repeating the last frame forever
Fix | take_reply() reads the FIFO between attempts (the peer's 'A' or next message ends the repeat); a finished board keeps answering (transport_idle())
Check it | comment out the take_reply() call in transmit(), build suite 2 method 3 with DEBUG=1, run the pair: it stops in the first echo
Restore | from fpga/sw/export: git checkout common/src/edhoc_rf_link.c, rebuild both images, rerun the same command: PASS. Compare the two logs at the point where the broken build stopped
Lesson | a link layer must keep listening while it waits

## Slide 17
2. Radio Link (8/8) What each fix changed
17
Link version | 1 MiB radio stream (TBD3)
no CRC, no watchdog | AEAD error after ~80 s (Problem 1)
+ CRC per frame | stalls after ~420 KB: deaf radio (Problem 2)
+ 2 s watchdog | completes (~135 s, 0 bad bytes) — hangs if both ends repeat
+ FIFO read while repeating | completes (~99 s), also with a slow peer (Problem 3)
The same link carries the handshakes of Lessons 3 and 4, so every pair uses these fixes.
Lesson: on real wires, check data end to end and recover from stuck hardware — do not trust the link layer of the chip alone.

## Slide 18
Outline
18
Application Channel
Radio Link
SD Card & FAT32
End-to-End Transfer
Making It Faster
Questions Behind the Project
Practice

## Slide 19
3. SD Card & FAT32 (1/8) What is on the card
19
Sectors (LBA) | Content | Written by
0 | MBR partition table | mksd.sh / sd_prep
2048 … 67583 (partition 1, 32 MiB, raw) | firmware image for SD boot | sd_boot.sh
67584 … end (partition 2, FAT32) | SEND.BIN (board A), RECV.BIN (board B) | your PC / the board
End-user flow: copy any file onto the card as SEND.BIN with a PC, put the card in board A, run — board B writes RECV.BIN on its card.
FAT32, so any PC reads and writes the files; the boot area stays raw.
Files up to 4 GiB (FAT32 limit); RAM use does not depend on the size.

## Slide 20
3. SD Card & FAT32 (2/8) Preparing a card — with or without a card reader
20
Run this — on a PC with a card reader
sudo fpga/sw/export/tools/mksd.sh /dev/sdX # erases the card: MBR + 32 MiB boot + FAT32
# then copy your file as SEND.BIN onto the FAT32 partition (label EDHOC)
Run this — no card reader: from the board, over JTAG
cd fpga/sw/export/tests
make sd_prep EXTRA_CFLAGS="-DSD_PREP_FORMAT -DSD_PREP_SEND=1048576" # format + 1 MiB test file
../common/board/run_one.sh build/sd_prep.elf 150
card: 61067264 sectors (29818 MiB)
formatting...
format OK
SEND.BIN: 1048576 bytes, CRC cffbfb2e
SD PREP OK
sd_prep writes the same layout as mksd.sh, plus a test SEND.BIN of known pseudo-random bytes.
-DSD_PREP_VERIFY later checks RECV.BIN on board B against the same bytes.

## Slide 21
3. SD Card & FAT32 (3/8) FAT32 on disk: from cluster to sector
21
MBR
LBA 0
boot image
2048 … 67583
reserved 32
boot sector, FSInfo
FAT 1
FAT 2
data: cluster 2, 3, 4 …
fat_lba = part_lba + reserved part_lba = 67584, reserved = 32
data_lba = fat_lba + nfats * fat_sz two FAT copies
LBA of cluster c = data_lba + (c - 2) * spc spc = sectors per cluster
FAT entry of cluster c = sector fat_lba + c / 128, byte (c % 128) * 4, low 28 bits
0 = free, 2 ... = next cluster, 0x0FFFFFFF = end of chain
Card (formatted by sd_prep, cluster size as Windows picks it) | spc | Cluster | 1 MiB file
board A, 31 GB | 32 | 16 KiB | 64 clusters
board B, 3.6 GB | 8 | 4 KiB | 256 clusters
All values come from the boot sector at part_lba (bytes 11, 13, 14, 16, 32, 36, 44, 48): fat32_mount() reads them and nothing else.

## Slide 22
3. SD Card & FAT32 (4/8) Fragmented files: following the cluster chain
22
root-directory entry, 32 bytes
53 45 4E 44 20 20 20 20 42 49 4E "SEND BIN" name, 8.3 form
20 attribute: archive
... bytes 20-21 / 26-27 first cluster, high / low 16 bits
... bytes 28-31 file size, little endian
dir entry
first = 5
FAT[5] = 6
FAT[6] = 7
FAT[7] = 12
FAT[12] = 13
FAT[13] =
0x0FFFFFFF
fat32_read()
if (f->pos && f->pos % cb == 0) { // crossed into the next cluster
fat_get(f->clus, &f->clus); // read its FAT entry
if (!valid(f->clus)) return FAT_ENOFS;
}
Reading follows any chain: a SEND.BIN a PC wrote in pieces works (host test "copy fragmented SEND.BIN"). Cost: one FAT sector per cluster, 63 extra reads for 1 MiB on card A (3 %).
Writing takes one contiguous run of free clusters: no FAT reads while streaming, the chain is written at commit.
Limit: a card whose free space exists only in pieces answers “no room” (FAT_ENOSPC). Copy the files off and reformat.

## Slide 23
3. SD Card & FAT32 (5/8) The SD driver and two bugs
23
Step | Command
Wake up in SPI mode | ≥ 74 clocks, then CMD0 (go idle) — retried
Check voltage / version | CMD8 → echo 0x1AA
Initialise | ACMD41 until ready; CMD58 → block addressing (SDHC)
Read / write one sector | CMD17 / CMD24, 512 B + CRC-16, then wait while busy
Bug 1: after power-up the card answers the first CMD0 with one junk byte (Lesson 2) → retry CMD0.
Bug 2: after a write the card holds the data line low while busy. The code waited only while it read exactly 0x00; the line is released in the middle of a byte (e.g. 0x0f), so the next command was sent too early and failed. Fix: wait until it reads 0xFF.
Both found on the board with a 30-line diagnostic that printed every raw byte.
Check bug 1: let CMD0 run once (t < 1 in tests/src/periph_spi.c), pull the card out and push it back in (this power-cycles only the card), run spi_test → R1 = 3f FAIL. Restore with git checkout. Check bug 2: sd_prep's verify reads back every written sector (section 4).

## Slide 24
3. SD Card & FAT32 (6/8) One sector over SPI
24
reading the FAT32 boot sector of the card
-> 51 00 01 08 00 01 CMD17 read block: 0x40 | 17, LBA 0x00010800 = 67584, CRC byte
<- FF 00 R1 = 0x00: command accepted
<- FF ... FF FE start token
<- 512 data bytes, CRC-16 we check the CRC-16 ourselves
-> 58 <LBA, 4 B> 01 CMD24 write block
<- 00 R1
-> FE, 512 data bytes, CRC-16
<- xxx0 0101 (0x05) data response: accepted
<- 00 00 ... 0F FF busy while the card programs: wait for FF (bug 2)
Every command is 6 bytes: 0x40 | index, a 32-bit argument, CRC-7 + stop bit. In SPI mode only CMD0 (95) and CMD8 (87) need a real CRC.
SDHC / SDXC cards take the sector number; old SDSC cards a byte address (LBA × 512). The CCS bit of CMD58 says which.
One sector per command: multi-block commands would save little, since the SD part is 5.7 s (read) and 6.5 s (write) of the 99.6 s transfer.

## Slide 25
3. SD Card & FAT32 (7/8) FAT32 in 512 bytes of RAM
25
One 512-byte sector buffer for everything: no FAT cache, no cluster buffer — the 64 KiB RAM cannot afford more.
Read SEND.BIN: find it in the root directory (8.3 name), follow its cluster chain sector by sector.
Write RECV.BIN: reserve one contiguous run of free clusters, write the data, then commit in a safe order:
1. data sectors
2. FAT chain
(both FAT copies)
3. directory entry
4. free the old
RECV.BIN
Rejected before commit (bad record, wrong CRC, lost link): only free clusters were written, so every file — including the old RECV.BIN — is unchanged.
Commit itself is several sector writes. An I/O error or power loss during commit can leave lost clusters or a half-written chain: run fsck.fat on a PC. This is not a power-loss-safe file system.

## Slide 26
3. SD Card & FAT32 (8/8) Testing the FAT32 code on the PC
26
cd tests && make fat32-host-test (excerpt of 15 checks)
copy fragmented SEND.BIN over old RECV.BIN PASS
RECV.BIN == SEND.BIN (pyfatfs) PASS
fsck.fat clean PASS
uncommitted write leaves files unchanged PASS
empty SEND.BIN -> new RECV.BIN PASS
1000-byte SEND.BIN -> new RECV.BIN PASS
format a junk card PASS
MBR: p1 raw at 2048, p2 FAT32 at 67584 PASS
copy on the formatted card PASS
missing file -> FAT_ENOENT PASS
FAT32 HOST TEST: PASS (0 failures)
Same fat32.c, with sd_read / sd_write going to a disk-image file.
Images made by mkfs.vfat, checked by fsck.fat and an independent FAT library (pyfatfs).
Does the test catch bugs? Two deliberately broken builds (no FAT mirroring, old chain not freed) both FAIL fsck.

## Slide 27
Outline
27
Application Channel
Radio Link
SD Card & FAT32
End-to-End Transfer
Making It Faster
Questions Behind the Project
Practice

## Slide 28
4. End-to-End Transfer (1/8) What goes over the air
28
Record | Plaintext | Purpose
0 | 4-byte length (0xFFFFFFFF = sender has no SEND.BIN) | receiver reserves space
1 … n | the file, 206 bytes per record, last one shorter | data
n + 1 | 4-byte CRC-32 of the file | end-to-end check, card to card
Every record is AEAD-protected (section 1) — that is the security. The CRC-32 checks the whole chain: SD read → radio → SD write.
Neither side holds more than one record and one sector: the same image moves 1 KB or 100 MB.
Receiver busy writing the card? The link just repeats fragments until it reads again — no extra flow control needed.

## Slide 29
4. End-to-End Transfer (2/8) From file bytes to radio frames
29
SD sector
512 B
fat32_read
206 B
AEAD record
206 + 16 = 222 B
rf_link_send
2 × 111 B
radio frame
127 B each
1 MiB, card A → card B | Count
SD sectors read on A / written on B | 2,048 / 2,048
records: 5,090 × 206 B + 1 × 36 B, plus the length and CRC records | 5,093
data frames ('D'), and as many 'A' frames back | 10,183
time per data frame: 99.6 s / 10,183 | ≈ 9.8 ms
Records do not line up with sectors (512 = 2 × 206 + 100): fat32_read copies across sector borders, and the one-sector buffer still reads each sector once.
No buffer grows with the file: one record, a few frames and one sector, the same for 1 KB or 4 GB.

## Slide 30
4. End-to-End Transfer (3/8) A check at every step
30
SEND.BIN: SD read
CRC-16 per sector
record: AEAD encrypt
—
fragments: radio
CRC-16 + FCS per frame
reassembly: seq, FIRST / LAST
order, nothing lost
record: AEAD decrypt
tag: authentic, in order
file: CRC-32
whole file, card to card
RECV.BIN: SD write + commit
data response 0x05, then commit
readback: sd_prep verify
every byte compared
Console line | Proves | Does not prove
XFER SENT (board A) | A read its file and every record was accepted by the link | anything about B's card
… CRC cffbfb2e OK (board B) | B received exactly the bytes of SEND.BIN | that they were stored
XFER RECV … -> RECV.BIN | B also committed RECV.BIN | that the card holds them correctly
sd_prep: 0 bytes differ | the stored file, read back, is right | —

## Slide 31
4. End-to-End Transfer (4/8) Build and run
31
Run this
cd fpga/sw/export/edhoc-authkem
make edhoc_authkem_initiator edhoc_authkem_responder SUITE=TBD3 EXTRA_CFLAGS=-DAPP_SD_XFER
../common/board/run_pair.sh xfer build-tbd3/edhoc_authkem_initiator.elf \
build-tbd3/edhoc_authkem_responder.elf 1500
# then check board B's card:
cd ../tests && make sd_prep EXTRA_CFLAGS=-DSD_PREP_VERIFY
BOARD=responder ../common/board/run_one.sh build/sd_prep.elf 20
Works with every suite of Lessons 3 and 4 (edhoc-wolfssl takes the same -DAPP_SD_XFER).
Board A needs SEND.BIN on its card; board B needs a FAT32 partition.

## Slide 32
4. End-to-End Transfer (5/8) Real run: 1 MiB from card A to card B
32
board A (initiator)
XFER: sending SEND.BIN, 1048576 bytes
PERF xfer_send 7465350439 cyc 99.538005 s 1048576 bytes 10534 B/s
PERF xfer_sd_part 427826394 cyc 5.704351 s
XFER SENT: 1048576 bytes, CRC cffbfb2e
board B (responder)
XFER: receiving 1048576 bytes
PERF xfer_recv 7469254102 cyc 99.590054 s 1048576 bytes 10528 B/s
PERF xfer_sd_part 490423540 cyc 6.538980 s
XFER RECV: 1048576 bytes -> RECV.BIN, CRC cffbfb2e OK
board B, sd_prep verify
card: 7569408 sectors (3696 MiB)
RECV.BIN: 1048576 bytes, CRC cffbfb2e, 0 bytes differ
SD PREP OK
1 MiB in 99.6 s = 10.5 KB/s, post-quantum TBD3 keys, AES-256-GCM.
SD time: 5.7 s read + 6.5 s write — the radio sets the pace.

## Slide 33
4. End-to-End Transfer (6/8) When something is missing
33
board A, card without FAT32
XFER: SD card not usable (-2)
XFER FAIL 3
board B
XFER: peer has no SEND.BIN
XFER FAIL 3
The sender announces “no file” (length 0xFFFFFFFF) instead of going silent: both boards stop cleanly in 3 s, no 5-minute timeout.
If board B's card fails, it still receives and checks the whole stream (CRC) and reports “not stored” — both sides stay in step.
A wrong CRC or a broken record: RECV.BIN is not written, the old one stays.

## Slide 34
4. End-to-End Transfer (7/8) When storage fails: a real run
34
Example output — board A
XFER: sending SEND.BIN, 1048576 bytes
XFER SENT: 1048576 bytes, CRC cffbfb2e
APP DATA OK
Example output — board B, same run
XFER: receiving 1048576 bytes
XFER: SD write failed at 618 (-1)
XFER: received 1048576 bytes, CRC cffbfb2e OK, not stored (-1)
XFER FAIL 3
APP DATA FAIL: 3
Example output — run_pair.sh
xferfix2 FAIL hs=1.236142s ... prk=match 122s no-APP-OK(xferfix2.res.log)
The communication path worked: the handshake, every record and the file CRC are fine. Storage failed: the first sector write (offset 618 = 3 records, past 512 B) was refused, so B kept receiving and checking but did not store.
Board A's “XFER SENT … APP DATA OK” is true and still not success. Judge a transfer by board B's last lines — and then read the file back (sd_prep verify).
Next steps: power-cycle and rerun; if it repeats, try another card or reformat it (sd_prep -DSD_PREP_FORMAT). Such failures can be intermittent — a card that failed once may pass the next run, which is why the readback step exists.

## Slide 35
4. End-to-End Transfer (8/8) Larger files: how to run the experiment
35
Step | How | Watch out
1. Make the file | copy it as SEND.BIN with a card reader, or sd_prep -DSD_PREP_SEND=<bytes> | FAT32: up to 4 GiB per file
2. Room on card B | free space ≥ file size, in one contiguous run (section 3) | else “no room” (FAT_ENOSPC): reformat B
3. Timeout | 4th argument of run_pair.sh: size / 10 KB/s + 60 s | 1 MiB ≈ 100 s → 200 s is safe
4. Run, keep logs | LOGDIR=xfer_runs ../common/board/run_pair.sh … | one log pair per run
5. Verify | sd_prep -DSD_PREP_VERIFY on board B (or sha256sum on a PC) | 0 bytes differ
6. Compare | PERF xfer_send / xfer_recv B/s and the STACK lines per size | RAM use should not grow
Units here: 1 MiB = 1,048,576 B; KB/s = 1,000 B/s; PERF prints B/s. Measured: 1 MiB in 99.6 s. Anything larger in these slides is an estimate from that rate until you measure it.

## Slide 36
Outline
36
Application Channel
Radio Link
SD Card & FAT32
End-to-End Transfer
Making It Faster
Questions Behind the Project
Practice

## Slide 37
5. Making It Faster (1/6) Measure first
37
Per radio frame (sender, 111 B of data) | Time
radio TX + hardware ACK | 7.0 ms
waiting for our 'A' | 1.75 ms
AES-256-GCM encryption (before tuning) | 3.1 ms
Cycle counters around each step, in a temporary instrumented build — not guesses. Numbers on this slide come from that build, not from TIMING=1.
Encrypting one 206-byte record took 6.5 ms = 490,000 cycles. That is far too slow for AES: something was wrong.
On-board micro-benchmark:
AES-256 block | GHASH multiply | Key schedule | GCM, 192 B
14,123 cyc | 19,777 cyc | 6,231 cyc | 490,695 cyc

## Slide 38
5. Making It Faster (2/6) The multiply trap
38
before (GHASH, aes_gcm.c)
uint64_t m = 0 - (bit & 1); // all ones if bit is set
zh ^= vh & m; // GCC turns this into bit * vh -> mul
after
static inline uint64_t top_mask(uint64_t x) { return (uint64_t)((int64_t)x >> 63); }
uint64_t m = top_mask(xh); // arithmetic shift: no multiply
zh ^= vh & m;
GCC recognises (0 - bit) & v and emits bit * v — usually faster. But this core's multiplier is bit-serial: ~64 cycles per mul.
Two muls per bit × 128 bits per GHASH block: 128 of every 155 cycles were multiplies.
Result: GHASH 19,777 → 3,326 cycles (6×). Same trap fixed in the CRC-32 code. Check with objdump -d … | grep mul.

## Slide 39
5. Making It Faster (3/6) Table-based AES
39
The byte-by-byte AES rounds became the 32-bit T-table form: each round is 16 table look-ups and XORs on whole columns.
One 1 KB table, built at first use from the S-box; the other three are its byte rotations.
Cycles | Before | After | Speed-up
AES-256 block | 14,123 | 2,224 | 6.3×
GHASH multiply | 19,777 | 3,326 | 5.9×
AES-256-GCM, 192-byte record | 490,695 | 91,741 | 5.3×
All known-answer tests (NIST GCM, RFC 3610, RFC 9529) still PASS. Bulk speed on the board now: encrypt 162 KB/s, decrypt 153 KB/s.
Cost: 1 KB of RAM — the largest builds still fit.

## Slide 40
5. Making It Faster (4/6) The radio side
40
Change | Why | Kept?
Burst SPI: whole FIFO in one command | 1 SPI byte per data byte instead of 3 | yes
No CSMA back-off before sending | two nodes taking turns: no one to avoid | yes
206-byte records | fill both radio fragments | yes
Turbo mode 625 kbit/s | ~2/3 of frames lost on these modules | no
Channel 26 (above Wi-Fi) | much worse than channel 11 here | no
SPI at 9.4 MHz | byte errors in the burst test | no
Each change tested on the boards; channel 11 has interference spells, so every experiment was compared with a control run made at the same time.

## Slide 41
5. Making It Faster (5/6) Result
41
Chart: 
| before | after
1 MiB card to card (KB/s) | 7.37 | 10.53
1 MiB, card A → card B, TBD3 | Before | After
Time | 142 s | 99.6 s
Throughput | 7.37 KB/s | 10.53 KB/s
Bytes wrong | 0 | 0
100 MiB (estimate, not measured) | ≈ 4 h | ≈ 2.8 h
+43 %: 104 s after these changes, 99.6 s with the link fix of section 2 (Problem 3). Handshakes got a little faster too (TBD3 1.37 → 1.25 s).
Check yourself: a TIMING=1 build prints PERF encrypt / decrypt in B/s; compare with the micro-benchmark of (1/6).

## Slide 42
5. Making It Faster (6/6) Where the limit is now
42
Raw radio, no ACK | Time per frame
full frame (116 B payload) | 6.3 ms
tiny frame (5 B payload) | 2.5 ms
From the slope: 32 µs per byte (250 kbit/s) plus ≈ 1.8 ms fixed per frame inside the radio chip.
Software is now ~1 ms of the ~9 ms per frame. The radio chip sets the speed.
A sliding window could save the ~19 % spent waiting for 'A' — risky with a one-frame receive buffer (Problem 3 in section 2 shows why).
Much faster needs different hardware, e.g. a wired link between the boards (UART on PMOD JB at Mbaud rates).

## Slide 43
Outline
43
Application Channel
Radio Link
SD Card & FAT32
End-to-End Transfer
Making It Faster
Questions Behind the Project
Practice

## Slide 44
6. Questions Behind the Project (1/3) The questions, and where they are answered
44
Question | Short answer | Lesson
Does EDHOC fit a small Rocket SoC with 32 KiB? | Only method 3 of suites 0/1/4; the rest need up to 61 KB → 64 KiB | 1, 2
Why not 100 MHz? | this implementation failed timing at 100 MHz and closes at 75 MHz | 1
Do all methods and suites work? | methods 0–3 × 9 suites run on two boards; the two RFC 9529 traces match byte for byte | 3
Does post-quantum EDHOC need a PSK? | no shared PSK; still trusted credentials and long-term ML-KEM private keys | 4
Is there a highest-security option? | TBD3, the strongest configured here: AES-256-GCM + ML-KEM-1024 + SHA-384 | 4
Where do large files live, how much RAM? | FAT32 on the SD card, streamed: RAM use is flat | 5
How long does each step take? | TIMING=1 prints PERF lines per step | 3, 4, 5
The questions were asked during the project; deviations.txt keeps the dated questions and answers.

## Slide 45
6. Questions Behind the Project (2/3) Limits to know before you reuse this code
45
Limit | Why | What to do
Random numbers (RFC 9528 §9.2) | this SoC has no TRNG; demo seeds come from the cycle counter | connect edhoc_platform_entropy() to real entropy
Post-quantum drafts | TBD1–3 unassigned; draft -01 may change | labels: one define; a new revision: full review + reference model
Radio speed | 250 kbit/s chip, ~10.5 KB/s end to end; 100 MiB ≈ 2.8 h (estimate) | a wired link (UART on PMOD JB) for much more
SD storage | commit is not power-loss safe; RECV.BIN needs contiguous free space | verify by readback; fsck.fat after a crash
32 KiB chips | only method 3 of suites 0/1/4 fits | use those builds, or give the chip more RAM
Boot from SD after power-up | the boot ROM sends CMD0 only once | load over JTAG (Lesson 2), or add a CMD0 retry to sdboot and rebuild the bitstream

## Slide 46
6. Questions Behind the Project (3/3) Reproduce everything
46
Step | Lesson | You should see
1. Clone [GitHub URL], build the bitstream, program both boards | 1 | timing met, jtag_test PASS
2. Toolchain, peripheral + crypto tests | 2 | every test PASS
3. EDHOC pairs, RFC 9529 test | 3 | PASS per pair, RFC9529 PASS
4. AuthKEM TBD1–3, reference model | 4 | prk=match, REFERENCE MODEL: PASS
5. Prepare cards, transfer, verify RECV.BIN | 5 | XFER RECV … OK, then 0 bytes differ
Every number in these lessons comes from such runs; the log format (PERF / STACK lines) and the scripts (run_pair.sh, perf_table.py) let you compare yours line by line.
VERBOSE=1 run_pair.sh ... shows both consoles live; a DEBUG=1 build adds every intermediate value.

## Slide 47
Outline
47
Application Channel
Radio Link
SD Card & FAT32
End-to-End Transfer
Making It Faster
Questions Behind the Project
Practice

## Slide 48
7. Practice (1/3) Exercises
48
Exercise 1:
Send a real file (a PDF, an image) from card A to card B with TBD3. Compare the two files on a PC (sha256sum).
Exercise 2:
Build the radio link without the CRC (remove seal and the check). Stream 1 MiB. What fails, after how long? Restore the file afterwards.
Exercise 3:
Measure KB/s for 64 KiB, 256 KiB and 1 MiB. Is the speed constant? Estimate the time for 100 MB.

## Slide 49
7. Practice (2/3) What to put in the report
49
Exercise 1: both consoles, the two sha256 values, the time and KB/s.
Exercise 2: the console at the failure and your explanation.
Exercise 3: a table and a chart of size vs. time; your 100 MB estimate.

## Slide 50
7. Practice (3/3) Answer notes
50
Exercise | What you should see | Why
1. Real file | identical sha256 on both files; ≈ 100 s per MiB plus a few seconds of handshake | CRC-32 and AEAD protect the path; the radio sets the pace
2. No CRC | sooner or later an AEAD failure on B (record at <n> failed (113)) — or, on a lucky run, none | a flipped SPI bit is no longer caught before the AEAD sees it
3. Sizes | about the same B/s for every size | the cost is per frame; nothing in RAM grows with the file
Restore after exercise 2: from fpga/sw/export, git checkout common/src/edhoc_rf_link.c, rebuild both images, rerun: XFER RECV … OK.
Negative cases to recognise: no SEND.BIN → both stop with XFER FAIL 3 in seconds; B's card fails → B says “not stored” while A says SENT (section 4, (7/8)); a broken record → B rejects it and keeps the old RECV.BIN.

## Slide 51
51
Today’s lesson highlight:
PRK_out → EDHOC_Exporter → K_app / IV_app; 206-byte AEAD records, nonce from direction + sequence number.
Radio link made reliable with a CRC per frame, a 2-second radio watchdog and reading the FIFO while repeating; SD driver fixed (CMD0 retry, busy wait).
FAT32 in one 512-byte buffer: SEND.BIN → RECV.BIN, committed only when the CRC matches.
1 MiB card to card with TBD3: 99.6 s, 0 bytes wrong; +43 % after removing hidden multiplies, table AES and the link fix.
A transfer succeeded only when board B says RECV … OK and the read-back matches — the sender's “SENT” is not enough.
Before real use: a real entropy source, and final post-quantum code points.
End of the course
Thank you for following all five lessons

## Slide 52
THANK YOU
52
[YYYY/MM]