## Slide 1
2026/12
「Course」
EDHOC on a Rocket RV64 SoC
1
Khai-Duy Nguyen
「 Lesson 2 」 Software environment and tests

## Slide 2
2
Today’s lesson purpose:
Install the bare-metal RISC-V toolchain and find your way around the firmware tree (fpga/sw/export).
Understand how one image is built: compiler flags, linker script, startup code, stack check.
Configure your own two boards, run a first program end to end, then check the peripherals and every crypto primitive on the board.
Prerequisite: Lesson 1 (both boards programmed with the EDHOC bitstream)

## Slide 3
Outline
3
Toolchain & Repository
Your Own Boards
Build System
Board Tools
Peripheral Tests
Crypto Tests
Practice

## Slide 4
Outline
4
Toolchain & Repository
Your Own Boards
Build System
Board Tools
Peripheral Tests
Crypto Tests
Practice

## Slide 5
1. Toolchain & Repository (1/6) The RISC-V GCC toolchain
5
git clone https://github.com/riscv-collab/riscv-gnu-toolchain
cd riscv-gnu-toolchain
./configure --prefix=$HOME/opt/riscv --with-multilib-generator="rv64imac-lp64--"
make -j$(nproc) # newlib (bare-metal) toolchain
export PATH=$HOME/opt/riscv/bin:$PATH
riscv64-unknown-elf-gcc --version # ours: 15.1.0
Bare metal: no operating system, no C library at run time — the firmware brings its own memcpy, printf (kprintf) and startup code.
Target: rv64imac / lp64, the small Rocket of Lesson 1 (no floating point).
Toolchain somewhere else? Pass the prefix instead of PATH: make CROSS_COMPILE=/opt/riscv/bin/riscv64-unknown-elf-
Also needed: OpenOCD (JTAG), Vivado (programming), Python 3 (host tests).

## Slide 6
1. Toolchain & Repository (2/6) The firmware tree: fpga/sw/export/
6
Directory | What it is
edhoc-wolfssl/ | EDHOC RFC 9528, methods 0–3, all 9 cipher suites (Lesson 3)
edhoc-authkem/ | post-quantum EDHOC AuthKEM, suites TBD1–TBD3 (Lesson 4)
tests/ | peripheral tests, crypto known-answer tests, SD card preparation (sd_prep)
common/ | shared by all three: startup, linker, drivers, CBOR, EDHOC core, crypto, radio link, SD/FAT32, board scripts
tools/ | mksd.sh — prepares a microSD card on a PC
docs/slides/ | these lessons, PPTX and PDF
deviations.txt | the questions asked during the project and how each was answered (dated log)
Everything is vendored: no submodules, nothing to download at build time.
The packages share common/, so copy export/ as a whole.

## Slide 7
1. Toolchain & Repository (3/6) What is in common/
7
Folder | Contents
src/, include/ | crt0.S startup, kprintf, libc stubs, UART/radio transport, MRF24J40 driver, SD card, FAT32, application channel, timing
linker/ | main.lds + memory.lds: one image in the 64 KiB scratchpad
mk/ | rv64.mk (toolchain, flags), rules.mk (compile / link rules)
edhoc/, cbor/ | EDHOC core shared by both packages, deterministic CBOR
crypto/ | SHA-256/384, HMAC/HKDF, AES-CCM/GCM, KMAC — written for this tree, small
externals/ | Monocypher (ChaCha20, Ed25519), curve25519-donna, mlkem-native
board/ | run_one.sh, load_both.sh, program_two.tcl, sd_boot.sh, c232hm.cfg, boards.env, perf_table.py
One copy of each piece of code: both EDHOC packages and the tests link the same files.

## Slide 8
1. Toolchain & Repository (4/6) Memory layout of one image
8
stack (grows down)
← _ram_end = 0x8001_0000
free (painted 0x5A5A5A5A)
.bss (zeroed)
.rodata / .data
.text (code)
← 0x8000_0000
The linker script places code, data and zeroed data from the bottom of the scratchpad; the stack grows down from the top.
Each build reserves a stack size (STACK_SIZE, per suite and role). The link fails if image + reserve do not fit:
common/linker/main.lds
ASSERT((_end <= (_ram_end - __stack_reserve)),
"ERROR: Program + stack exceeds RAM. Reduce the image or lower STACK_SIZE.")
The linker checks that the program and the configured stack reserve fit. Whether the real stack stays inside that reserve is measured on the board (next slides).

## Slide 9
1. Toolchain & Repository (5/6) Will my build fit? Check it yourself
9
Run this
cd fpga/sw/export/edhoc-wolfssl
make edhoc_m3_initiator CRYPTO_SUITE=4
riscv64-unknown-elf-size build/edhoc_m3_initiator.elf
grep -m1 __stack_size build/edhoc_m3_initiator.map
Example output — this revision
text data bss dec hex filename
25523 0 1640 27163 6a1b build/edhoc_m3_...
... __stack_size = 0x1500 (= 5,376 B)
Build (initiator) | text | bss | image | stack reserve | total | left of 64 KiB
suite 4, method 3 | 25,523 | 1,640 | 27,163 | 5,376 | 32,539 | 32,997 B
suite 25, method 0 | 46,457 | 1,752 | 48,209 | 12,544 | 60,753 | 4,783 B
text = code + constants, data = initialised variables, bss = zeroed variables (in RAM, not in the file). The ELF file (37,128 B here) also holds symbols; the .bin (25,536 B) is what gets loaded. Default flags: no TIMING, DEBUG or APP options, TRANSPORT=rf.
The table sums section bytes; alignment can add padding. The linker checks _end - 0x80000000 + __stack_reserve ≤ 65536 (see the map). Also check the board's stack peak against the reserve (next slide).
Why 64 KiB? Most configurations exceed 32 KiB including stack. A small initiator fitting alone does not prove its responder fits: check both roles.

## Slide 10
1. Toolchain & Repository (6/6) Startup code and the stack check
10
common/src/crt0.S (outline)
_prog_start:
la sp, _sp // stack at the top of the scratchpad
// clear .bss
// paint all free RAM [_end, _ram_end) with 0x5A5A5A5A
call main
end of every EDHOC run
STACK peak 5376 B, reserve 8448 B, free 25856 B, headroom 20480
At the end of a run the firmware looks for the first word that is no longer 0x5A5A5A5A: that is the deepest the stack ever went (stack_highwater()).
peak = measured use; reserve = what the build set aside; headroom = how far the stack could still grow into free RAM.
A run whose peak is over its reserve prints OVERRAN-RESERVE and run_pair.sh fails it. The reserves in this course are measured peak + 25 %.
This line comes right after the handshake. A second one, STACK whole run, at the very end also covers the application step (echo, file transfer).

## Slide 11
Outline
11
Toolchain & Repository
Your Own Boards
Build System
Board Tools
Peripheral Tests
Crypto Tests
Practice

## Slide 12
2. Your Own Boards (1/3) Find your four serial numbers
12
Run this
cd fpga/sw/export
./common/board/list_boards.sh
Example output — our lab, yours differ
C232HM JTAG FTA6GPSN (C232HM-DDHSL-0)
Arty console 210319B4A439 /dev/ttyUSB4
C232HM JTAG FTA6JVAK (C232HM-DDHSL-0)
Arty console 210319B269F6 /dev/ttyUSB1
boards.env key | What it is | Which line
INITIATOR_CONSOLE | board A's own USB serial (its console) | Arty console
RESPONDER_CONSOLE | board B's own USB serial | Arty console
INITIATOR_SERIAL | C232HM cable on board A's PMOD JD | C232HM JTAG
RESPONDER_SERIAL | C232HM cable on board B's PMOD JD | C232HM JTAG
Which is which? Unplug board B's two USB plugs, run the script again: what is left belongs to board A.
Roles: board A = initiator (sends SEND.BIN), board B = responder (writes RECV.BIN). Label the boards.

## Slide 13
2. Your Own Boards (2/3) Write them into boards.env and check
13
Edit — fpga/sw/export/common/board/boards.env (ships with ours: replace all four)
INITIATOR_SERIAL=FTA6JVAK # C232HM on board A <- yours
RESPONDER_SERIAL=FTA6GPSN # C232HM on board B <- yours
INITIATOR_CONSOLE=210319B269F6 # Arty A <- yours
RESPONDER_CONSOLE=210319B4A439 # Arty B <- yours
Run this
cd fpga/sw/export/tests && make gpio_test
BOARD=initiator ../common/board/run_one.sh build/gpio_test.elf 5
BOARD=responder ../common/board/run_one.sh build/gpio_test.elf 5
You see | Meaning / fix
LEDs walk on board A, then B; console text each time | all four serials right
LEDs walk on the other board | the two cable serials are swapped
LEDs walk, console prints nothing | console serials swapped or wrong
“console … not found” | a console serial is not plugged in or mistyped
OpenOCD error, no LEDs | cable serial wrong, JD wiring, or FPGA not programmed (“dtmcontrol is 0”: Lesson 1, section 6)

## Slide 14
2. Your Own Boards (3/3) Lab: your first program, end to end
14
Objective | load one program into board A and read its result
Starting state | both FPGAs programmed (Lesson 1); boards.env filled in; toolchain and OpenOCD installed
Run this
cd fpga/sw/export/tests
make gpio_test
BOARD=initiator ../common/board/run_one.sh build/gpio_test.elf 5
Example output — board A (shortened)
=== GPIO test (0x64002000, 8 pins) ===
output_en : got=ff want=ff PASS
all high : got=ff want=ff PASS
walking ones (watch the LEDs):
walk: PASS
GPIO TEST: PASS (0 failures)
What it proves: JTAG loading works (the program runs at all), UART0 and the console path work (you read it), the GPIO block answers on the bus (read-back PASS), and the pins reach the LEDs (you see them walk).
What it does not prove: anything about SPI, the radio or the SD card — those have their own tests (section 5).
If it fails: nothing printed → (2/3) table; a FAIL line → that register or pin; LEDs dark but PASS → the pins of the bitstream (Lesson 1, section 4).

## Slide 15
Outline
15
Toolchain & Repository
Your Own Boards
Build System
Board Tools
Peripheral Tests
Crypto Tests
Practice

## Slide 16
3. Build System (1/4) How a package Makefile is put together
16
Makefile
entry point
mk/config.mk
suite, profile, stack,
sources, includes
common/mk/rv64.mk
toolchain, -march,
transport, link flags
common/mk/rules.mk
compile, link, .bin,
flags stamp
mk/targets.mk
one target per
method × role
Run this
cd fpga/sw/export/edhoc-wolfssl
make edhoc_m3_initiator CRYPTO_SUITE=2 # -> build/edhoc_m3_initiator.elf
make edhoc_m3_responder CRYPTO_SUITE=2 # same build/ folder, no 'make clean'
cd ../edhoc-authkem
make edhoc_authkem_initiator SUITE=TBD3 # -> build-tbd3/edhoc_authkem_initiator.elf
Blue = shared by both packages (common/mk), yellow = per package.
Output per target: .elf (load over JTAG), .bin (SD boot), .map (who uses how many bytes).

## Slide 17
3. Build System (2/4) Compiler and linker flags
17
common/mk/rv64.mk (excerpt)
ARCH_FLAGS = -march=rv64imac_zicsr_zifencei -mabi=lp64 -mcmodel=medany
LDFLAGS = $(ARCH_FLAGS) -flto -T $(COMMON)/linker/main.lds
LDFLAGS += -nostartfiles -nostdlib -nodefaultlibs
LDFLAGS += -Wl,--defsym=__stack_size=$(STACK_SIZE)
LDFLAGS += -Wl,--gc-sections -Wl,-Map=$(BUILD_DIR)/$(TARGET).map
Flag | Why
-mcmodel=medany | code and data at 0x8000_0000 (not near address 0)
-Os, -flto, --gc-sections | optimise for size, link-time optimisation, drop every unused function → small images
-nostdlib -nostartfiles | no C library, the tree's own crt0.S
--defsym=__stack_size | stack reserve for the ASSERT in the linker script
-Map=…map | where every byte went — first stop when an image grows

## Slide 18
3. Build System (3/4) Switching suite, method or role: no make clean needed
18
All targets of a package share one build/ folder and differ only in flags (method, role, suite). Make by itself compares only file times, so it would reuse objects built with other flags — an image of the wrong method, no error.
The build keeps an empty stamp file named after a hash of the flags. New flags → new stamp name → every object is older than its stamp → everything recompiles.
Check it: run ls build/.cflags-*, build with another CRYPTO_SUITE, run it again — the name changes and every object compiles again.
common/mk/rules.mk
CFLAGS_STAMP = $(BUILD_DIR)/.cflags-$(shell echo '$(CFLAGS) $(INCLUDES)' | md5sum | cut -c1-12)
$(CFLAGS_STAMP): | $(BUILD_DIR)
@rm -f $(BUILD_DIR)/.cflags-*
@touch $@
$(BUILD_DIR)/%.o: %.c $(CFLAGS_STAMP)
@$(CC) -c $(CFLAGS) $(INCLUDES) $< -o $@

## Slide 19
3. Build System (4/4) Build options
19
Option | Values | Effect
CRYPTO_SUITE= (wolfssl) | 0 1 2 3 4 5 6 24 25 | EDHOC cipher suite (default 2)
SUITE= (authkem) | TBD1 TBD2 TBD3 | post-quantum suite (default TBD2)
TRANSPORT= | rf ¦ uart | radio on PMOD JC (default) or 3 wires on JB (921,600 baud; EXTRA_CFLAGS=-DUART1_BAUD=…)
DEBUG=1 |  | step-by-step prints, incl. PRK_out
TIMING=1 |  | time of every message step (Lessons 3, 4)
APP_FILE_BYTES=n | bytes | stream n test bytes after the handshake
EXTRA_CFLAGS=-DAPP_SD_XFER |  | send SEND.BIN card to card (Lesson 5)
PROFILE=production | + PROVISION_SRC | refuse demo keys, require a real random source
Full lists: edhoc-wolfssl/README.md, edhoc-authkem/README.md.

## Slide 20
Outline
20
Toolchain & Repository
Your Own Boards
Build System
Board Tools
Peripheral Tests
Crypto Tests
Practice

## Slide 21
4. Board Tools (1/4) Scripts in common/board/
21
Script | Does
program_two.tcl | Vivado batch: program both FPGAs with one bitstream
run_one.sh <elf> [s] | load one board over JTAG, run, print its console
load_both.sh <A.elf> <B.elf> | load responder, then initiator (handshake runs)
boards.env | FTDI serials of the two C232HM cables
c232hm.cfg | OpenOCD config: cable + RISC-V debug tap
sd_boot.sh | write a firmware .bin to the SD boot partition
perf_table.py <logdir> | TIMING=1 logs → one table of message times
Plus tools/mksd.sh (card on a PC) and tests/sd_prep (card from the board, Lesson 5).

## Slide 22
4. Board Tools (2/4) What happens when you load a program
22
OpenOCD
connects to the
C232HM by serial
halt
stop the core
load_image
ELF → scratchpad
0x8000_0000
resume
jump to
_prog_start
console
cat /dev/ttyUSBn
57600 baud
common/board/run_one.sh (core)
stty -F $TTY 57600 raw -echo clocal -crtscts
cat $TTY > $LOG & # start listening first
openocd -c "adapter serial $SERIAL" -f c232hm.cfg -c "poll off" -c "halt" \
-c "reg mstatus 0x0" -c "reg mie 0x0" -c "reg mtvec 0x80000000" \
-c "load_image $ELF" -c "resume 0x80000000" -c "shutdown"
sleep "$SECS"; tr -d '\r' < "$LOG"
Interrupts off and the trap vector reset before loading: a previous program cannot fire into the new one.
The console is opened before the program starts, so no early line is lost.

## Slide 23
4. Board Tools (3/4) Reading the console
23
initiator, suite 2, method 3
EDHOC OK!
PERF handshake_total 206069790 cyc 2.747597 s
PERF handshake_link 103475867 cyc 1.379678 s
PERF handshake_compute 102593923 cyc 1.367918 s
STACK peak 5376 B, reserve 8448 B, free 25856 B, headroom 20480
PERF encrypt 54759 cyc 0.000730 s 60 bytes 82191 B/s
APP DATA OK
PERF lines: label, cycles, seconds — and for transfers bytes and B/s. Seconds = cycles / 75 MHz.
total = whole handshake; link = waiting for the radio; compute = the rest.
STACK: the stack check from section 1.
OK / PASS / FAIL lines are what the sweep scripts look for.
Fixed line shapes make every run machine-readable: perf_table.py builds the tables of Lessons 3–5 from saved logs.

## Slide 24
4. Board Tools (4/4) Common problems
24
Symptom | Cause | Fix
OpenOCD: “dtmcontrol is 0” | FPGA not running the EDHOC bitstream (power-off) | program again (program_two.tcl)
No console text | console serial wrong in boards.env | list_boards.sh, then fix boards.env
LEDs react on the other board | cable serials swapped | swap them in boards.env
LIBUSB_ERROR_BUSY | Vivado GUI holds the JTAG port | close the hardware manager or reuse its server
TRANSPORT=uart run hangs | no wire between the boards | JB1 ↔ JB2 crossed between boards, plus GND
Link: “Program + stack exceeds RAM” | image + reserve > 64 KiB | smaller build or lower STACK_SIZE (check the peak first)
Run ends with OVERRAN-RESERVE | stack peak above its reserve | raise STACK_SIZE

## Slide 25
Outline
25
Toolchain & Repository
Your Own Boards
Build System
Board Tools
Peripheral Tests
Crypto Tests
Practice

## Slide 26
5. Peripheral Tests (1/3) Four programs, one per peripheral
26
Program | Checks | You should see
gpio_test | output enable, all low/high, walking ones (LEDs), XOR, patterns | PASS
uart_test | UART0 console, UART1 registers, optional loopback JB1–JB2 | PASS (loopback SKIP without jumper)
spi_test | SPI0 registers, real SD card answers CMD0 with R1 = 0x01 | PASS
jtag_test | loaded over JTAG at all; reads mhartid, marchid, misa | PASS
Run this
cd fpga/sw/export/tests
make periph # all four
BOARD=initiator ../common/board/run_one.sh build/spi_test.elf 3
Console output of each: Lesson 1, section 6.

## Slide 27
5. Peripheral Tests (2/3) How a test is written
27
tests/src/periph_gpio.c (simplified)
/* 2. walking ones — proves each pin is independently addressable */
kprintf(" walking ones (watch the LEDs):\r\n");
for (int i = 0; i < GPIO_WIDTH; i++) {
GPIO_REG(GPIO_OUTPUT_VAL) = 1u << i;
delay();
if ((GPIO_REG(GPIO_OUTPUT_VAL) & 0xff) != (1u << i))
fails++;
}
kprintf(" walk: %s\r\n", fails ? "FAIL" : "PASS");
Write a register, read it back, print PASS / FAIL per phase and one final verdict.
Something you can see: the LEDs walk.
A test that needs outside help (UART loopback, SD card) prints SKIP instead of FAIL when the help is missing.
SKIP is not PASS: that check did not run. The final PASS covers only the checks that ran — read every line, not just the last one.

## Slide 28
5. Peripheral Tests (3/3) If spi_test shows R1 = 3f or 7f
28
raw bytes after each command, initiator board
CMD0: 3f 1 ff ff ff ff ... <- first CMD0 after power-up
CMD0: ff 1 ff ff ff ff ... <- second CMD0
CMD8: ff 1 0 0 1 aa ff ... <- voltage check echoes 0x1AA
Right after the card powers up it can answer the first CMD0 with one junk byte (bit 7 clear, e.g. 0x3f). The card is fine.
spi_test, the firmware and the boot ROM all send CMD0 up to 10 times until R1 = 0x01, so normally you only see PASS.
If you still see 3f / 7f: check the card is pushed fully in and the PmodMicroSD sits in the top row of JA; then print the raw bytes (as above) — not every card answers at the same moment.
Rule of thumb for any SPI device: look at the raw bytes before blaming the hardware.

## Slide 29
Outline
29
Toolchain & Repository
Your Own Boards
Build System
Board Tools
Peripheral Tests
Crypto Tests
Practice

## Slide 30
6. Crypto Tests (1/5) What is tested, against which vectors
30
Primitive | Implementation | Test vectors
SHA-256 / SHA-384 | common/crypto | FIPS 180-4
HMAC-SHA-256 | common/crypto | RFC 4231, test case 1
HKDF-SHA-256 | common/crypto | RFC 5869, test case 1
AES-128-CCM | common/crypto | RFC 3610
AES-128-GCM / AES-256-GCM | common/crypto | NIST GCM spec, test cases 2 / 14
X25519 | curve25519-donna | RFC 7748 §6.1
ML-KEM-512 / 768 / 1024 | mlkem-native (FIPS 203) | FIPS 203 known answers + rejection
The tests link the same files the EDHOC firmware uses — not a separate copy — so a PASS here covers the code that runs in the handshake.

## Slide 31
6. Crypto Tests (2/5) crypto_test on the board
31
tests/build/crypto_test.elf
=== Classical crypto KAT (common/crypto, donna) ===
vectors: FIPS 180-4, RFC 4231, RFC 5869, RFC 3610, NIST GCM, RFC 7748
SHA-256 : PASS
SHA-384 : PASS
HMAC-SHA-256 : PASS
HKDF-SHA-256 : PASS
AES-128-CCM : PASS
CCM tag : PASS
CCM decrypt : PASS
AES-128-GCM : PASS
GCM tag : PASS
GCM decrypt : PASS
AES-256-GCM : PASS
GCM tag : PASS
GCM decrypt : PASS
X25519 shared : 8917229 cycles
X25519 : PASS
CRYPTO TEST: PASS (0 failures)
AEAD tests check three things: ciphertext, tag, and that decrypting the expected ciphertext verifies.
On a mismatch the test prints got and want, so the console alone is enough to debug.
X25519 key agreement: 8.9 M cycles = 0.12 s at 75 MHz.

## Slide 32
6. Crypto Tests (3/5) mlkem_test on the board
32
tests/build/mlkem_test.elf
=== ML-KEM (FIPS 203, mlkem-native) test levels 512/768/1024 ===
-- ML-KEM-512 (pk=800 sk=1632 ct=768) --
keypair KAT : PASS
encaps KAT : PASS
decaps : PASS
reject KAT : PASS
-- ML-KEM-768 (pk=1184 sk=2400 ct=1088) --
keypair KAT : PASS encaps KAT : PASS decaps : PASS reject KAT : PASS
-- ML-KEM-1024 (pk=1568 sk=3168 ct=1568) --
keypair KAT : PASS encaps KAT : PASS decaps : PASS reject KAT : PASS
MLKEM TEST: PASS (0 failures)
Three security levels in one image: the library is compiled three times with different prefixes (mlk512_, mlk768_, mlk1024_).
reject KAT: a corrupted ciphertext must give the defined pseudo-random key, not an error — FIPS 203 implicit rejection.
Needs a 16 KiB stack (ML-KEM-768 decapsulation is the deepest call).

## Slide 33
6. Crypto Tests (4/5) How a known-answer test is written
33
tests/src/crypto_classic.c (shortened)
static int test_x25519(void)
{
/* RFC 7748 section 6.1: Alice and Bob must agree on K */
static const uint8_t a_priv[32] = { 0x77,0x07,0x6D,0x0A, ... };
static const uint8_t b_pub[32] = { 0xDE,0x9E,0xDB,0x7D, ... };
static const uint8_t want[32] = { 0x4A,0x5D,0x9D,0x5B, ... };
uint8_t got[32];
curve25519_donna(got, a_priv, b_pub);
return report("X25519 ", got, want, 32); // PASS, or got/want dump
}
Inputs and expected output copied byte for byte from the standard.
One function per primitive, one report() that compares and prints.
Add a primitive: one more function and one more line in main().

## Slide 34
6. Crypto Tests (5/5) Tests on the PC
34
Host test | What it runs | You should see
make loopback-test (wolfssl) | initiator + responder as two threads, one suite × method per run, PRK_out compared | PRK_out match -> PASS
make unit-test, loopback-test (authkem) | encodings, KEM, error messages; full 5-message handshake, per suite | PASS
make rfc9529-test | every byte of the RFC 9529 example traces (Lesson 3) | PASS for suites 0, 2, 24
make fat32-host-test (tests/) | FAT32 code on a real disk image, checked with fsck.fat | every check PASS
Same C files as the firmware, compiled for the PC: seconds per run, a debugger, no boards needed.
Rule used throughout: host test first, then the board.

## Slide 35
Outline
35
Toolchain & Repository
Your Own Boards
Build System
Board Tools
Peripheral Tests
Crypto Tests
Practice

## Slide 36
7. Practice (1/3) Exercises
36
Exercise 1:
Build the toolchain, then make periph crypto in tests/. Note each image size from the size output.
Exercise 2:
Run all six test programs on both boards and collect the console output.
Exercise 3:
Add a SHA-256 test for the empty string (FIPS 180-4 example) to crypto_classic.c and make it PASS on the board.
Then break one byte of the expected value: what does the console show?

## Slide 37
7. Practice (2/3) What to put in the report
37
Exercise 1: toolchain version, the build commands, image sizes.
Exercise 2: the six console logs per board; explain any SKIP.
Exercise 3: your test function, the PASS output and the FAIL output with the broken byte.

## Slide 38
7. Practice (3/3) Answer notes
38
Exercise | What you should find | Why
1. Sizes | each image's text + bss from riscv64-unknown-elf-size; crypto_test and mlkem_test are the largest test images | they link the most crypto code
2. Six tests | every final line PASS on both boards; uart_test shows UART1 loop: SKIP without the jumper | SKIP = not run; nothing failed
3. SHA-256('') | want = e3b0c442 98fc1c14 9afbf4c8 996fb924 27ae41e4 649b934c a495991b 7852b855 → PASS | FIPS 180-4 example
3. broken byte | “SHA-256 …: FAIL”, then got and want, differing in that byte; final line CRYPTO TEST: FAIL (1 failures) | the test compares every byte and counts failures
Restore after exercise 3: undo the broken byte (or, from fpga/sw/export, git checkout tests/src/crypto_classic.c), rebuild, run: PASS again.

## Slide 39
39
Today’s lesson highlight:
Bare-metal RV64IMAC firmware: own startup, own libc pieces, one image in the 64 KiB scratchpad; the linker refuses image + stack reserve that do not fit, the STACK line shows the real peak.
One shared common/ tree; makefiles split into shared flags/rules and per-package targets; a flags stamp prevents stale objects.
Load over JTAG with run_one.sh; PERF / STACK / PASS lines make every run machine-readable.
You can now: set up boards.env for your boards, check whether a build fits and how much stack margin it has, load either board, and tell PASS, FAIL and SKIP apart in peripheral and crypto test output.
Next lesson:
「 Lesson 3 」 EDHOC (RFC 9528) on two boards

## Slide 40
THANK YOU
40
2026/12